## Slide 1: IST346: Server and Server Operating Systems

## Slide 2: Agenda
Understand the difference between servers and workstations
Discuss the common IT issues surrounding servers, including server virtualization
Outlay the various types of servers and operating systems

## Slide 3: Servers vs. Workstations

## Slide 4: What is a Server?
A server is a computer that supplies services to users via other computers, called clients. The clients are usually workstations (but not always).
A service is the function of the server. Services are what differentiates a structured computing environment from bunch of standalone computers on a network.
Popular services:
  Infrastructure: DHCP, DNS, Authentication, LDAP
  User: File Sharing, Printing, Web, Database, Email

## Slide 5: How are they different?
A Workstation has…
A Server has…
One “concurrent” user
A broad range of roles
  Email, Web, Word, etc…
Hardware optimized for interactivity
Reliability and uptime are lower priority
Several “concurrent” users
A narrow range of roles
  “File” server / “web” server
Hardware optimized for background processing
Reliability and update are high priority

## Slide 6: What Makes a Server a Server?
Server hardware:
  Extensible/expandable
  Increased performance (multiple cpus/cores)
  High performance I/O (input/output)
  High availability
  Maintenance contracts
  Management options
Services!!!

## Slide 7: The Client-Server Model
filer.fauxco.com
192.168.1.10
ctl02.fauxco.com
192.168.1.202
ctl03.fauxco.com
192.168.1.203
ctl04.fauxco.com
192.168.1.204
ctl05.fauxco.com
192.168.1.205
Server
Workstations

## Slide 8: Servers and their role in IT

## Slide 9: Servers:
Service 100’s if not 1,000’s of users
Require high reliability and security due to lengthy required uptimes for services.
Are expected to last longer than workstations
Cost much more than workstations
Cost accounting for servers is spread over the users who use them, not responsibility of IT.

## Slide 10: Servers:
Have different OS configurations than workstations
Are deployed in a data center
Have disk backup systems
Have maintenance contracts with the Vendor

## Slide 11: Server-Class Hardware
More internal space.
More CPU/Memory.
  More / high-end CPUs.
  More / faster memory.
High performance I/O.
  PCIe/x vs. PCI
  SCSI/FC vs. IDE/Sata
Rack mounted (typically)
Redundancy
  RAID Storage arrays / Hot-swappable hardware.
Highly Tested, Certified
Management interfaces

## Slide 12: Servers belong in a server room!
Servers should be kept in their own rooms: data centers
DC’s are special homes for servers
They have:
  Adequate power
  UPS / Generators
  Fire Suppression
  Air Conditioning
  Networking
  Physical Security
More on data centers later in the semester
Notes: Picture of the google data center.

## Slide 13: Nobody likes to work in a data center
They’re cold, noisy and cramped.
Efficient space for servers, no so much for people!
Remote Administration is key
  Access to system consoles remotely
    SSH / VNC on Linux
    Remote Desktop on Windows
  Hard Boot (Power On/Off ) servers can be problematic
  Media insertion can be an issue, too.
  There’s a Data Center Unit Later in the course, so more is to come.

## Slide 14: Maintenance Contracts
Let’s face it, hardware fails. Longer running time  Greater chance of failure
Hardware on maintenance contracts will guarantee replacement parts and may even include a service dispatch technician (on site).
Mission critical servers should have 2-4 hour response, on-site coverage. NBD, SBD, 9x5, 24x7,4 hours, 2 hours.
2 Hour response means vendor will respond within 2 hours.
Having spare parts on hand, “on the shelf” is a common practice.
Service contracts can be purchased from the hardware vendor, but also from 3rd parties.
Notes: NBD – next business day
SBD – same business day

## Slide 15: What is most likely to fail on a server?
Anything with “moving parts”
#1 – Disk Drive (lots of moving parts)
  Redundant Disks RAID 1, 5, 6 are common
  Server keeps working despite disk failure
  Most servers have hot-plug in / hot-spare technology
  Good idea to keep a spare disk on the shelf “OTS.”
  The more disks in your RAID, the better the performance.
#2 – Power supply (fans, power surges)
  Redundant power supplies means server can continue to operate if one PS fails.
  Most Servers have hot plug-in technology for PS
  Redundant PS’s should have separate power cords on separate power sources.
#3 – Network Interface Card (NIC)
  Redundant NIC’s with automatic failover are common.

## Slide 16: Server Virtualization – Are you Hip?
http://www.youtube.com/watch?v=57XDSrwEdRg

## Slide 17: Virtualization of Servers
Problem with physical server hardware is:
  Management, the more servers you have, the harder they are to manage.
  It can be grossly under-utilized in CPU, Memory or Storage for a given service
  When it goes over resource capacity, you need to buy new hardware or upgrade.
  Space, physical servers require more space in your data centers.
Organizations have been turning to virtual server infrastructure to address these limitations.
  Capacity can be scaled up or down based on the needs of the service at the times they are required
  Maximizes the investment in hardware – get the most bang for your buck.
  Makes it easer to power on/off servers and deal with media insertion issues.
  Virtualized servers have the same hardware configuration

## Slide 18: SU virtual server infrastructure

## Slide 19: Types of Servers: Hardware Options Operating Systems

## Slide 20: Rack Mountable Servers
Server hardware in configured in to fit in a Rack chassis.
Measured in Rack Units (U’s)
Servers Accessible via Front/Back
Server can be maintained, repaired and upgraded while in the rack.

## Slide 21: Does it take long to rack servers?
Let’s see the process in high-speed: http://youtu.be/xs6mWS2Jv-Y

## Slide 22: Server Appliances
A server appliance is dedicated hardware and software
The appliance fits a specific role: File Server, Web server, Load Balancer, Firewall, Router, etc.
You can use a OTS server to perform these tasks, so why buy?
Advantages:
  Easy to setup, Reliable, Performance
Disadvantages
  Cost, Integration

## Slide 23: Blade Servers
Very high density: They offer the maximum horsepower for the allotted space.
Pros:
  Flexible
  High-Performance
  Can Grow with your needs
Cons:
  Expensive
  High power / cooling demands
  Vendor Lock-in

## Slide 24: Server Operating Systems
Unix-Like:
  Ubuntu, Red Hat Enterprise, Sun Solaris, IBM AIX
Windows
  Windows Server 2003 / 2008 Standard, Enterprise, and Datacenter editions.
Embedded Operating Systems in appliances
  Used in appliances: Routers, Firewalls, Load Balancers, Video streaming, etc.
  Linux, FreeBSD, Windows
It should be noted that each operating system specializes at different services, and no one OS is good at everything.

## Slide 25: Finally a word from our sponsor:

## Slide 26: Servers: Not just for business anymore

## Slide 27: Questions?
If lawyers are disbarred and clergymen defrocked, doesn't it follow that electricians can be delighted, musicians denoted, cowboys deranged, models deposed, tree surgeons debarked and dry cleaners depressed?

## Slide 28: IST346:
Data Centers

## Slide 29: Data Centers
What is a datacenter?
  Page 129, “ a data center is a place where you keep machines that are a shared resource”
  A.K.A
    Server room
    Machine room
    Server closet (hopefully not literally a “closet”)

## Slide 30: Data Centers - Options
Build
Rent
$100 - $400 per square foot to build
  This is known as a “co-location Facility”
  IaaS
  Paas
you don’t care about the physical servers, just the services running on them. Everything you do is for the services.

## Slide 31: Data Center- Major Components
What makes a data center more than just a closet with a bunch of servers?
    Location
    Access
    Security
    Power, Cooling, Humidity
    Fire Suppression
    Racks
    Cable Management
    Communications
    Console Access
    Workbench
    Tools, parts, etc

## Slide 32: Location
Talking geography and on site.
  If your area is susceptible to flooding, don’t put your data center in the basement.
“One company I’ve read about has two data centers, one in Florida and one in Colorado. They change primary data centers every 6 months.”
Why?
Florida  hurricanes
Colorado snow storms.

## Slide 33: Access
What type of access is required?
  Wheelchair, ramps, loading docks to unload equipment?
Some equipment is wider than the average sized door. Need double-doors.
Restrict access to people who don’t need it.

## Slide 34: Security
What type of security do you require?
  Numeric key pads – bad idea. Anyone can share the code. No way of knowing who came in.
  Keys, - better, at least you know who you gave the key to originally
  Card swipes – even better, logs entry information and controls access
  Proximity detectors – better still, same advantages as card swipes but more convenient
  Biometrics – almost there. Thumb print reader or voice recognition. Disadvantages ?
  Two Factor, -best, something you have and something you know. A numeric keypad that requires both a static or non-changing code and a one-time-password security token.

## Slide 35: Cooling
For every watt of power used in the data center, you need to plan for the same amount of power to cool your equipment.
Direct your cool air where you need it
New types of cooling concepts, “cool the servers, not the entire room” (SU Green DC)
Rear door heat exchangers. Cools only the servers and not surrounding room air. Most efficient.

## Slide 36: Large Data Center Air Conditioner and Rear Door Heat Exchanger

## Slide 37: Hot and Cold Isles and Humidity
Cold air goes in front of rack, heated by server, exited out back.
Arrange your data center so the backs of the racks are towards each other. This forms hot and cold isles.
Easier to collect the hot air. Heat rises.
Keep server room humidity between 45% - 55%. Too low, static, too high, condensation.

## Slide 38: Power
Multiple sources of electricity.
  Multiple feeds from multiple substations.
  Generator, not only for emergencies but also for normal operations.
  What type of power does it produce, do you need? 110V, 220V, 480V?
  Discussion is driven by what type of power your servers require. Not all servers require 110V “standard line power”.
  Can you use DC power? 240 Volts? More efficient than 110V. Save up to 4% in electric usage.
  Be “Green” in your data center. Where does your electricity come from?

## Slide 39: Power
Do you have a Uninterruptable power supply (UPS)? How big?
How long does it need to last, 10 minutes, 1 hour, 4 hours?
Varies depending if you have a generator or not.
Do you have automatic transfer switches, (ATS)?
  Switches that ‘sense’ if line power or in Syracuse, National Grid power if present, and if not, automatically starts generator and transfers load. When line power returns, shuts off generator and returns load to line power.

## Slide 40: Power Distribution Unit (PDU)
Looks like a power strip, much more.
Can be horizontally or virtually mounted
Monitor, record, and control each outlet remotely via network.
Should have two per server, one connected to line power and one connected to UPS / Generator power
A PDU is not a UPS. They’re different.

## Slide 41: Monitor your Power

## Slide 42: Fire Suppression
Require Fire suppression methods; required by law /code
Conventional (Water and Sprinklers) = Bad
Many other methods
  CO2 & Halon, good for servers, bad for people
  Conventional extinguishers
  Consult local fire authorities
Cost plays a large factor.

## Slide 43: Racks
The ‘spine’ of the data center
Dictate other components
  Wiring, cooling, power, etc
  Not inexpensive, up to $10,000 per rack with required products (power, cooling, networking, etc)
Standard 19” wide, width of standard mountable equipment. 19” between posts.
Some telecomm equipment is wider. Special order
May purchase racks wider and deeper than your needs as to leave room for networking, power, cooling, etc.
2 or 4 posts
  4 is better but more expensive.
Rack equipment in U’s or rack units,
  1.75 inches per “U”
  Can use square nuts or screws to mount equipment

## Slide 44: Rack Cooling
Racks are typically open at the bottom to allow cool air to flow in.
Heat rises exits out the back
Not a location to run wires. Run cabling overhead with above-the-racks wire trays
Keep doors and sides on if using raised floor, off it using standard air-conditioning
Monitor temperature inside racks
iSchool uses a device called “Weather Goose”

## Slide 45: Racks Determine Cable Management
A good cabling job is a pleasure to work with.
Don’t ‘build-your-own’ cables. Purchase cat6 (category 6) cables.
Purchase special cable management products.
Easily identify which cable connects to what.
Color code or label your cables
Separate power from network cables. Power down one side, network cables down the other

## Slide 46: Cable Management Images

## Slide 47: Come up with cabling Guidelines
Blue / Green – production network
Red / Orange – storage network (iSCSI)
Yellow – KVM
White – Private NAT

## Slide 48: And why do we need cabling guidelines?
Bob, can you connect the email server to the new storage device, it’s the yellow wire.

## Slide 49: Communications
Put a telephone in your server room incase you need to call someone in for assistance or be speaking with a vendor while standing in front of the server.
“Bridge” the telephone line into a infrequently used circuit to save money.
Don’t rely on cell phones. Can be difficult to hear plus more interference in server room.

## Slide 50: Console Access - KVM
Discussed already
In-band vs. out-of-band management
KVM usage
If no KVM or out-of-band management, consider using a ‘crash cart’ or setup cart.
  Basically a vertical cart with a keyboard, mouse, and monitor used when 1st setting up servers or if they crash so bad you can’t use other management techniques

## Slide 51: Workbench, Tools, Parts
Have a place where your staff can test out or ‘burn in’ a server before putting it into production.
Place to troubleshoot failed servers
Have extra patch cables, nuts, bolts, “spare parts” on hand.

## Slide 52: Alternative data centers
Sometimes you have to think “outside the box”…or in these cases, in a different box!

## Slide 53: Summary
Data center is much more than a standard room or closet.
Many things make a server room unique.
$100 / $400 or more per square foot to create a server room.
Look for alternatives, outsource
If you are going to build it, do it right the first time.

## Slide 54: Questions?
“There are 10 kinds of people in the world, those that understand binary and those that don’t”